## Slide 1
2020 NRRA Pavement Workshop Series
Presented
By
Choon Park, Ph.D.
Founder / Principal Geophysicist
September 3, 2020
Seismic Approach to
Quality Management of Asphalt Pavement (HMA)

## Slide 2
MnDOT Contract No. 1034287 Federal Project Number: TPF-5 (341) Execution: January, 2020 - December, 2021
Principal Investigator (PI): Choon Park, Ph.D., Founder/Principal Geophysicist, Park Seismic LLC*
Co Investigator (CI): Nils Ryden, Ph.D., Research Director Norrfee Tech AB, Lund, Sweden**
Co Investigator (CI): Josefin Starkhammar, Ph.D., Founder Norrfee Tech AB, Lund, Sweden**
Administration Staff: Jin Park, Ph.D., Operations Manager/Financial Coordinator, Park Seismic LLC*
*Prime Contractor: Over-sighting Project, Development of Software Package
**Sub Contractor: Development of Hardware System
Seismic Approach to Quality Management of HMA

## Slide 4
Hot Mix Asphalt (HMA) Pavement
Stiffness (e.g., Vs) and Thickness (H)
Construction and Maintenance

## Slide 5
  Multichannel Analysis of Surface Waves (MASW) (Park et al., 1999)
  Shear-wave velocity (Vs) (1D, 2D, and 3D)
  Vs  Direct indicator of “stiffness” [e.g., Young’s (E) and shear ()]
Seismic Approach  MASW
MASW

## Slide 6
Pavement MASW (Ryden et al., 2004)
I-70 (Manhattan, KS)
Lamb wave (A0)
Contact measurements with accelerometer and a small hammer.
~0.5 Hour
~0.1 Hour
Field Measurement
Data Process

## Slide 7
Conventional (Contact) Approach  Survey Time
(12 ft x 300 ft)
3 ft x 3 ft resolution
Total 400 survey points
Acquisition: 400 x 0.5 hr = 200 hrs.
Processing: 400 x 0.1 hr = 40 hrs.
Total: 240 hrs.
(Ryden et al., 2004)

## Slide 8
Non-Contact Pavement MASW
(Ryden et al., 2006)
Surface wave
Surface wave
Leaky
surface wave

## Slide 9
Shear wave velocity (m/s)
Test line 4.0 m
Non-Contact-Rolling Pavement MASW
(Bjurström and Ryden, 2017)
48 MEMS microphone array (1-cm spacing)
Solenoid impact source
SLOW!!!
Moving Speed < 0.5 MPH

## Slide 10
Bouncing ball source!
Rolling Impact Source*  “Bouncing Steel Ball”
*A 48-channel (CH) system with MEMS Microphone Array (MMA) (Ryden et al., 2019)  “SYS-RYD-2019”
48-CH MMA

## Slide 11
THIS PROJECT
On-Board Real Time Display
5 – 20
MPH
MMA: MEMS Microphone Array (16-CH/array?)

## Slide 12
This (Non-Contact) Approach  Survey Time
(12 ft x 300 ft)
3 ft x 3 ft resolution
Total 400 survey points
Acquisition: 18 seconds @ 20 km/hr speed
Processing: 200 seconds @ 0.5 sec/record
Total: 218 seconds ( < 4 minutes)

## Slide 13
240 Hours
218 seconds (< 4 min.) !!!
Survey Time | Contact vs. Non-Contact

## Slide 14
Estimated Presentation of Results
 Velocity (Vs) and Temperature 
12 ft
12 ft

## Slide 15
Estimated Presentation of Results
 Modulus (Shear & Young’s) 
12 ft
12 ft

## Slide 16
Estimated Presentation of Results
 Thickness (Lamb & Impact Echo) 
Lamb
Impact Echo (IE)
12 ft
12 ft

## Slide 17
New System for This (HMA) Project  “SYS-HMA”
A 64-Channel (2 x 32-Channel, 16-bit) system (expandable up to 96-Channel)
Multiple (e.g., 4) arrays to Cover a 12-ft lane simultaneously
GPS for survey coordinates and geo-location, and IR sensor for HMA temperature.

## Slide 18
Software Package  “ParkSEIS-HMA”

## Slide 19
Direct Air Wave Domination
RAW
MUTE
Direct air wave
Surface (Lamb) wave
Direct air wave
Surface (Lamb) wave
Direct
air wave

## Slide 20
RAW
MUTE-1
MUTE-2
Air Wave Handling  Complications
?

## Slide 21
H = 0.260 m @ 7841 Hz
Thickness (H)
Velocity (Vs)
Surface Wave Analysis 
Velocity (Vs) and Thickness (H)
Spectral (Impact Echo) Analysis 
Thickness (H)
Impact Echo (IE)  Alternative H Evaluation
Amplitude (%)

## Slide 22
Jan-2020
Dec-2021
Project* Progress
Hardware  Under field testing with old system to finalize the 1D array configuration (e.g., N-channel, channel spacing, etc.)
Software  ACQ and QA/QC module under development
1st Joint Field Test (JFT)  Fall, 2020 (“Remotely” Joint)
*Year 1: Completion of 1D System
*Year 2: Completion of 2D System
Now

## Slide 24
Hardware Development and Field Testing
Nils Ryden, Ph.D., and Josefin Starkhammar, Ph.D.
Norrfee Tech AB, Lund, Sweden